## Slide 1
CONFERENCE PAPER PROPOSAL · B
How Far Does the Model Hold?
Robustness of Multihorizon Failure Intelligence
Under Realistic Operating Conditions
Building on: Shikdar & Laaksonen (2026)
Target: IEEE SGES · PMAPS · IEEE PES GM Workshop
Est. Timeline: 2 Weeks · No field data required
1 / 8

## Slide 2
01 · THE ORIGINAL PAPER
The Calibration Strength We Are Building On
The original paper's most important practical feature is not its AUC score — it is its probability calibration.
Isotonic regression ensures that when the model says 'this battery has a 70% chance of failing,' that probability is honest. Without calibration, a high AUC score is meaningless for dispatch decisions.
"A well-calibrated model is one that can be trusted
— not just one that scores well on a leaderboard."
Calibration Method
Isotonic
Regression
probability calibration
AUC Score
0.89–0.94
NASA 18650 baseline
Training Data
Lab cycling
only
controlled conditions
Dispatch Policy
Binary
risk ≤ τ
deploy or reject
2 / 8

## Slide 3
02 · THE GAP
The Weakest Assumption in the Paper
The model was trained and evaluated exclusively on clean,
controlled laboratory cycling data.
WHAT THE MODEL WAS TRAINED ON
WHAT REAL BATTERIES EXPERIENCE
Full charge / discharge cycles
Fixed C-rate throughout
Consistent rest periods
Controlled room temperature
Partial charges at varying depths
Variable and irregular load
Random rest periods, overnight stops
Temperature fluctuations
The calibration quality under this shift is completely unknown. No operator can trust a model whose reliability degrades in unknown ways.
3 / 8

## Slide 4
03 · HOW WE TEST IT
Synthetic Perturbation — No Field Data Needed
STEP 1
Start with lab data
Take the existing NASA lab cycling data as the foundation. The trained hazard model remains unchanged.
STEP 2
Generate synthetic profiles
Systematically perturb the lab data: partial cycles at 3 depth-of-discharge levels, randomized rest periods, temperature noise. 4 severity levels from mild to aggressive.
STEP 3
Measure calibration degradation
At each severity level, measure ECE (Expected Calibration Error) and AUC. Test whether recalibration on a small synthetic sample can recover reliability.
No field data required at any stage. All profiles generated synthetically from existing lab observations.
4 / 8

## Slide 5
03 · HOW WE TEST IT
2-Week Execution Plan
1
Days 1–3
Perturbation Scheme Design
Define 4 severity levels. Code partial-cycle generator, rest randomizer, temperature noise injector from NASA lab base data.
2
Days 4–7
Profile Generation & Inference
Generate 500–1000 synthetic profiles per severity level. Run each through the trained hazard model. Record raw probability outputs.
3
Days 8–10
Calibration Measurement
Compute ECE and AUC at each severity level. Test recalibration: retrain isotonic regression on 10% synthetic data, remeasure ECE.
4
Days 11–14
Analysis & Writing
Produce reliability diagram per severity level. Plot ECE vs. perturbation severity curve. Write paper in IEEE 6-page format.
5 / 8

## Slide 6
04 · OUR CONTRIBUTION
What We Add to the Field
①
Operational boundary map
The first characterization of how much deviation from lab conditions a multihorizon hazard model can tolerate before calibration becomes untrustworthy.
②
Recalibration recovery finding
Whether a small-sample recalibration step is sufficient to maintain reliability under operational shift — a practical recommendation for any future deployment.
③
This is an extension, not a critique
We characterize the limits of a promising framework — the necessary step between lab validation and deployment. The original author commissioned this.
④
Either outcome is publishable
Model holds → field deployment is credible. Model degrades → operators know exactly where the limits are. Both findings are valuable and honest.
6 / 8

## Slide 7
EXPECTED OUTPUT
Calibration Error vs. Operational Perturbation Severity (Illustrative)
Chart: 
| Lab (baseline) | Mild | Moderate | Aggressive
ECE — No Recalibration | 0.04 | 0.09 | 0.16 | 0.28
ECE — After Recalibration | 0.04 | 0.06 | 0.09 | 0.14
Lower ECE = better calibration. This chart shows whether recalibration can recover reliability as operating conditions deviate from lab.
7 / 8

## Slide 8
Conference B · Summary
One model.
Four stress levels.
Does calibration survive?
GAP ADDRESSED
Lab-only data; calibration under real conditions untested
METHOD
Synthetic perturbation at 4 severity levels, ECE measurement
DATA NEEDED
NASA lab data (existing) + synthetic profiles (generated)
TIMELINE
14 days
TARGET VENUE
IEEE SGES / PMAPS / IEEE PES GM Workshop
8 / 8